## Slide 1: Characterization and Transformation of Unstructured Control Flow in GPU Applications
Haicheng Wu, Gregory Diamos, Si Li, Sudhakar Yalamanchili
Computer Architecture and Systems Laboratory
School of Electrical and Computer Engineering
Georgia Institute of Technology
Special thanks to our sponsors: NSF, LogicBlox, and NVIDIA

## Slide 2: Outline
Introduction
GPU Control Flow Support
Control Flow Transformations
Experimental Evaluation
Conclusions & Future Work

## Slide 3: Understanding Unstructured Control Flow is Critical
Branch Divergence is key to high performance in GPU
  Its impact is different depending upon whether the control flow is structured or unstructured
Not all GPUs support unstructured CFG directly
  Using dynamic translation to support AMD GPUs*
* R. Dominguez, D. Schaa, and D. Kaeli. Caracal: Dynamic translation of runtime environments for gpus. In Proceedings
of the Fourth Workshop on General Purpose Processing on Graphics Processing Units, pages 5–11. ACM, 2011.

## Slide 4: Our Contributions
Assesses the occurrence of unstructured control flow in several GPU benchmark suites
Establishes that unstructured control flow can degrade performance in cases that do occur in real applications.
Implements an unstructured control flow to a structured control flow compiler transformation.
  Research the impact of unstructured control flow
  Execution portability via dynamic translation

## Slide 5: Outline
Introduction
GPU Control Flow Support
Control Flow Transformations
Experimental Evaluation
Conclusions & Future Work

## Slide 6: Structured/Unstructured Control Flow
Structured Control Flow has a single entry and a single exit
Unstructured Control Flow has multiple entries or exits
Exit
Entry
if-then-else
Entry/Exit
for-loop/while-loop
do-while-loop
Entry
Exit

## Slide 7: Sources of Unstructured Control Flow (1/2)
goto statement of C/C++
Language semantics
Not all conditions need to be evaluated
Sub-graphs in red circles have 2 exits
B1
bra cond1()
B4
bra cond4()
B2
bra cond2()
B3
bra cond3()
B5
……
entry
exit
if (cond1() || cond2())
&& cond3() || cond4()))
{
……
}

## Slide 8: Sources of Unstructured Control Flow (2/2)
Compiler Optimizations
  Inline for() into main()
  loop2 has 2 exits

## Slide 9: Impact of Branch Divergence in Modern GPUs
fall-through part first
branch target part next
re-converge at last

## Slide 10: Re-convergence in AMD & Intel GPUs
AMD IL does not support arbitrary branch
  It also uses ELSE, LOOP, ENDLOOP, etc.
Intel GEN5 works in a similar manner
ige r6, r4, r5
if_logicalz r6
uav_raw_load_id(0) r11, r10
uav_raw_load_id(0) r14, r13
iadd r17, r16, r8
uav_raw_store_id(0) r17, r15
endif
if (i < N)
{
C[i] = A[i] + B[i]
}
C Code
AMD IL

## Slide 11: Re-converge at immediate post-dominator
Entry
Entry
Entry
Entry
Entry
Entry
Entry
B1
B1
B1
B1
B1
B1
B1
B2
B2
B2
B3
B3
B4
B4
B5
T0
T1
T2
T3
T4
T5
T6
B2
B3
B1
bra cond1()
B4
bra cond4()
B2
bra cond2()
B3
bra cond3()
B5
……
entry
exit
B5
B3
B3
B3
B4
B4
B5
B5
Exit
Exit
Exit
Exit
Exit
Exit
Exit
Entry
Entry
Entry
Entry
Entry
Entry
Entry
B1
B1
B1
B1
B1
B1
B1
B2
B2
B2
B2
B3
B3
B3
B4
B4
B5
T0
T1
T2
T3
T4
T5
T6
B3
B4
B3
B4
B5
B3
B5
Exit
Exit
Exit
Exit
Exit
Exit
Exit
1
2
3
4
5
6
7
8
9
10
11
12
B5
B5
B3
B3
B3
B4
B4
B5
B5
B3
B3
B3
B4
B4
B5

## Slide 12: Alternatives: Executing Arbitrary Control Flow on GPUs
The simplest method is to let compilers have the option to produce IR code only containing structured control flows. This IR code then can be compiled into different back-ends.
Use a JIT compiler to dynamically transform the unstructured control flow to structured control flow online when necessary.
Develop a new technology to fully utilize the early re-convergence opportunity.
Increasing Efficiency

## Slide 13: Outline
Introduction
GPU Control Flow Support
Control Flow Transformations
Experimental Evaluation
Conclusions & Future Work

## Slide 14: Overview of the Transformation
It is based on the work of Zhang and Hollander*
It includes 3 sub transformations
  Cut: move the outgoing edge of a loop to the outside of the loop
  Backward Copy: move the incoming edges of a loop to the outside of the loop
  Forward Copy: handles the unstructured control flow in the acyclic CFG
We also need to locate structured/unstructured sub CFG
* F. Zhang and E. H. D’Hollander. Using hammock graphs to structure programs. IEEE Trans. Softw. Eng., pages 231–245, 2004.

## Slide 15: Cut Transformation
B6
B1
Use three flags to label the location of the loop exits
  Flag1: True False
  Flag2: True False
  Exit: True False
Combine all exit edges to a single exit edge
Use conditional check to find the correct code to execute after the loop
B2
B3
B4
B5
B1
B2
B6
B3
B4
B5
B8
B7
B7
B8

## Slide 16: Backward Copy Transformation
B3
B4
B5
B4
B3
B5
B3
B4
B5
B1
B2
B6
Use loop peeling to unravel the first iteration
Point all incoming edges to the peeled part
B3’
B4’
B5’
B3
B4
B5
B1
B2
B6

## Slide 17: Forward Copy Transformation
Duplicate Node B5
Duplicate Node {B3, B4, B5, B6}
B1
bra cond1()
B4
bra cond4()
B2
bra cond2()
B3
bra cond3()
B5
……
entry
exit
B1
bra cond1()
B4
bra cond4()
B2
bra cond2()
B3
bra cond3()
B5
……
entry
exit
B5
……
B5’
……
B4’
bra cond4()
B3’
bra cond3()
B5’’
……
B5’’’
……
B4
bra cond4()
B3
bra cond3()
B5
……
B5’
……

## Slide 18: The Relation between Forward Copy and Re-converge at the immediate post-dominator
B1
bra cond1()
B4
bra cond4()
B2
bra cond2()
B3
bra cond3()
B5
……
entry
exit
B1
bra cond1()
B2
bra cond2()
entry
exit
B4’
bra cond4()
B3’
bra cond3()
B5’’
……
B5’’’
……
B4
bra cond4()
B3
bra cond3()
B5
……
B5’
……
B5
B3
B3
B3
B4
B4
B5
B5
Exit
Exit
Exit
Exit
Exit
Exit
Exit
Entry
Entry
Entry
Entry
Entry
Entry
Entry
B1
B1
B1
B1
B1
B1
B1
B2
B2
B2
B2
B3
B3
B3
B4
B4
B5
Original CFG
After Forward Copy
/ DF Spanning Tree
Re-converge at the
immediate post-dominator
They are the same as the DS Spanning Tree
Forward Copy can be used to research the impact of immediate post-dominator

## Slide 19: Control Tree
We also need the Control Tree* to locate structured and unstructured CFG
* S. Muchnick. Advanced Compiler Design Implementation. Morgan Kaufmann Publishers, 1997.
{B3}: Block
{B3}: Self-Loop
{B3}: Block
{entry, B1-B4, exit}: Block
{exit}: Block
{entry}: Block
{B1-B4}: Do-While Loop
{B4}: Block
{B1}: Block
{B2}: Block
{B1-B3}: Unstructured
entry
B1
exit
B2
B4
B3

## Slide 20: Put Them Together
{B3}: Block
{B3}: Self-Loop
{B3}: Self-Loop
{B3}: Block
{B2}: Block
{entry, B1-B4, exit}: Block
{exit}: Block
{entry}: Block
{B1-B4}: Do-While Loop
{B1-B3}: Unstructured
{B4}: Block
{B1}: Block
{B2-B3}: If-Then
Identify unstructured branches and structured control flow patterns
Collapse the detected structured control flow pattern into a single node
Use three sub transformations to turn the unstructured control flow into structured control flow
entry
B1
exit
B2
B4
B3
{B1-B3}: Unstructured
B3
{B3}
{B3}
{B1-B3}: If-Then-Else
{B2}: Block
{B3}: Self-Loop
{B3}: Block

## Slide 21: Outline
Introduction
GPU Control Flow Support
Control Flow Transformations
Experimental Evaluation
Conclusions & Future Work

## Slide 22: Experimental Setup
Benchmarks:
  Cuda SDK 3.2
  Parboil 2.0
  Rodinia 1.0
  Optix SDK 2.1
  Some third party applications
Tools:
  NVCC 3.2 compiles CUDA to PTX
  Ocelot 1.2.807* is used for:
    PTX transformation
    Functional emulation
    Trace generation
* G. Diamos, A. Kerr, S. Yalamanchili, and N. Clark. Ocelot: A dynamic compiler for bulk-synchronous applications in heterogeneous systems. In Proceedings of PACT ’10, pages 353–364. ACM, 2010.

## Slide 23: Existence of Unstructured Control Flow
Suite | Number of Benchmarks | Number of Transformed Benchmarks
CUDA SDK | 56 | 4
Parboil | 12 | 3
Rodinia | 20 | 9
Optix | 25 | 11
Total | 113 | 27
27 out of 113 benchmarks have unstructured control flow
  The transformation is required to support CUDA on all GPUs
Complex applications are more likely to include unstructured control flow

## Slide 24: Transformation Statistics (1/3)
Benchmark | Branch Instruction | Cut | Forward Copy | Backward Copy | old code size | new code size | Static Code Expansion (%)
mergeSort | 160 | 0 | 4 | 0 | 1914 | 1946 | 1.67
particles | 32 | 0 | 1 | 0 | 772 | 790 | 2.33
Mandelbrot | 340 | 6 | 6 | 0 | 3470 | 4072 | 17.35
eigenValues | 431 | 0 | 2 | 0 | 4459 | 4519 | 1.35
bfs | 65 | 1 | 0 | 0 | 684 | 689 | 0.73
mri-fhd | 163 | 1 | 0 | 0 | 1979 | 1984 | 0.25
tpacf | 37 | 0 | 1 | 0 | 476 | 499 | 4.83
mcrad | 415 | 11 | 10 | 0 | 4552 | 5238 | 15.07
sphyraena | 1125 | 4 | 3 | 0 | 4393 | 4418 | 0.57
Renderer | 7148 | 943 | 179 | 0 | 70176 | 111540 | 58.94
mcx | 178 | 0 | 9 | 0 | 2957 | 5527 | 86.91
CUDA SDK
Parboil
3rd Party

## Slide 25: Transformation Statistics (2/3)
Benchmark | Branch Instruction | Cut | Forward Copy | Backward Copy | old code size | new code size | Static Code Expansion (%)
heartwall | 144 | 0 | 2 | 0 | 1683 | 1701 | 1.07
hotspot | 19 | 1 | 0 | 0 | 237 | 242 | 2.11
particlefilter_naive | 29 | 3 | 5 | 0 | 155 | 203 | 30.97
particlfilter_float | 132 | 2 | 4 | 0 | 1524 | 1566 | 2.76
mummergpu | 92 | 2 | 26 | 0 | 1112 | 2117 | 90.38
srad_v1 | 34 | 0 | 1 | 0 | 572 | 595 | 4.02
Myocyte | 4452 | 2 | 55 | 0 | 54993 | 62800 | 14.2
Cell | 74 | 1 | 0 | 0 | 507 | 512 | 0.99
PathFinder | 9 | 1 | 0 | 0 | 136 | 141 | 3.68
Rodinia

## Slide 26: Transformation Statistics (3/3)
Benchmark | Branch Instruction | Cut | Forward Copy | Backward Copy | old code size | new code size | Static Code Expansion (%)
glass | 157 | 0 | 7 | 0 | 4385 | 4892 | 11.56
julia | 1634 | 14 | 22 | 0 | 14097 | 18191 | 29.04
mcmc_sampler | 101 | 0 | 3 | 0 | 4225 | 4702 | 11.29
whirligig | 143 | 0 | 8 | 0 | 4533 | 5303 | 16.99
whitted | 173 | 0 | 6 | 0 | 5389 | 5841 | 8.39
zoneplate | 297 | 0 | 3 | 0 | 3397 | 3400 | 0.09
collision | 101 | 0 | 4 | 0 | 2585 | 2595 | 0.39
progressivePhotonMap | 127 | 0 | 4 | 0 | 3905 | 3960 | 1.41
path_trace | 29 | 1 | 0 | 0 | 1870 | 1875 | 0.27
heightfield | 46 | 1 | 0 | 0 | 1761 | 1771 | 0.57
swimmingShark | 51 | 1 | 0 | 0 | 1990 | 2000 | 0.5
Optix

## Slide 27: Static Code Expansion Caused by Forward Copy
The average is 17.89%
Chart: 
| mergeSort | particles | Mandelbrot | eigenValues | tpacf | heartwall | particlfilter_naive | particlfilter_float | mummergpu | srad_v1 | Myocyte | glass | julia | mcmc_sampler | whirligig | whitted | zoneplate | collision | progressivePhotonMap | mcrad | sphyraena | Renderer | mcx
Static Code Expansion (%) | 1.6719 | 2.3316 | 17.3487 | 1.3456 | 4.8319 | 1.0695 | 30.9677 | 2.7559 | 90.3777 | 4.021 | 14.1964 | 11.5621 | 29.0416 | 11.2899 | 16.9865 | 8.3875 | 0.088313 | 0.38685 | 1.4085 | 15.0703 | 0.56909 | 58.9432 | 86.9124

## Slide 28: Dynamic Code Expansion (1/2)
We do not know the technique to re-converge at the earliest point yet
B5
B3
B3
B3
B4
B4
B5
B5
Exit
Exit
Exit
Exit
Exit
Exit
Exit
Entry
Entry
Entry
Entry
Entry
Entry
Entry
B1
B1
B1
B1
B1
B1
B1
B2
B2
B2
B2
B3
B3
B3
B4
B4
B5
We measure the time the application runs in this region
1. Unstructured Branch
2. Threads are divergent

## Slide 29: Dynamic Code Expansion (2/2)
Benchmark | Dynamic Code Expansion Area (instructions) | Original Dynamic Instruction Count | Dynamic Code Expansion Area (%)
Mandelbrot | 86690 | 40756133 | 0.21%
heartwall | 749028 | 121606107 | 0.62%
Renderer | 462485018 | 549222644 | 84.21%
Myocyte | 205924 | 7893897 | 2.61%
mummergpu | 11947451 | 53616778 | 22.28%
mcx | 13928549604 | 20820693688 | 66.90%
tpacf | 2082509458 | 11724288389 | 17.76%
Unstructured branches are not executed
Threads do not diverge
Small static expansion, but large dynamic expansion

## Slide 30: Opportunities
We modified the Ocelot emulator to force benchmark mummergpu to re-converge as early as possible.
New version reduces 14.2% of dynamic instructions
Opportunity for optimization

## Slide 31: Outline
Introduction
GPU Control Flow Support
Control Flow Transformations
Experimental Evaluation
Conclusions & Future Work

## Slide 32: Conclusions
The current support of Unstructured Control Flow in GPU is inefficient
  Some are incapable of executing unstructured CFG directly
  Some use inefficient method to re-converge threads
An unstructured to structured transformation is valuable for both understanding its impact and execution portability
  Three sub transformations and Control Tree are used
  Forward Copy is widely needed and may cause large code expansion.

## Slide 33: Future Work
Develop the technique to re-converge at the earliest point
  Need the support of both compiler and hardware
  Find the earliest re-converge point
  Efficiently compare thread PC and schedule threads
Reverse the transformation to optimize the performance
  Structured -> Unstructured
  Enable it to Re-converge earlier by using above technique

## Slide 34: Reverse the Transformation
B1
bra cond1()
B2
bra cond2()
B4
bra cond4()
B3
bra cond3()
B5
……
entry
exit
B5
……
B4
bra cond4()
B3
bra cond3()
B1
bra cond1()
B4
bra cond4()
B2
bra cond2()
B3
bra cond3()
B5
……
entry
exit
B5
……
B4
bra cond4()
B3
bra cond3()
B5
……
B5
……
B5
……
B5
……
B5
……
B5
……
B5
……
B5
……
B5
……
B5
……
B4
bra cond4()
B3
bra cond3()
B4
bra cond4()
B3
bra cond3()
B5
……
B4
bra cond4()
B3
bra cond3()
B5
……
B4
bra cond4()
B3
bra cond3()
B5
……
B4
bra cond4()
B3
bra cond3()
if (cond1() ) {
if (cond2()) {
if (cond3()) {
……
} elseif (cond4()) {
……
}
}
} elseif (cond3()) {
……
} elseif (cond4()) {
……
}
Find identical nodes
Merge these nodes
Inefficient Code

## Slide 35: Questions?
Contact Us:
{hwu36, gregory.diamos, sli, sudha}@gatech.edu
Download GPU Ocelot
http://code.google.com/p/gpuocelot/