# Node Management Design 2.0

Futures Laboratory

Argonne National Laboratory

9700 S. Cass Ave.

Argonne, IL 60439

2/3/2003

## Summary

The Node Management subsystem is responsible for maintaining the centralized configuration of an Access Grid Node.  This implies a system that is aware of the various resources available in the node, which may be distributed over multiple machines.  These resources can be assigned to Services designed to enable sharing of the resource in a Venue.  Node Management consolidates the configuration of an Access Grid node and makes it available via a network interface.

|  | Requirement | Description |
| --- | --- | --- |
| 1.0 | Node Service |  |
| 1.1 | Add Services to and Remove Services from Node |  |
| 1.2 | Configure Services |  |
| 2.0 | Service Manager |  |
| 2.1 | Expose interface for configuring Services |  |
| 3.0 | Service |  |
| 3.1 | Expose interface for configuring a resource |  |

## Design

### Technology Decisions

The Node Management subsystem consists of multiple components, possibly distributed over multiple machines.  These components will be implemented in Python.  They will communicate using SOAP, which will enable third parties to develop interoperable services in any language.

### Module Decomposition

The Node Management subsystem of the Access Grid consists primarily of a Node Service, a collection of Service Managers, and several Services.  Services are responsible for delivering data from resources local to the machines in a Node; they are configured by the Node Service through Service Managers that run on each machine.

The Node Service has a network interface to permit communication with various clients, whether local or remote, GUI or otherwise. The Node Service maintains connections with Service Managers to discover resources available on their machines, and to add Services.  The Node Service also maintains connections to the Services running on individual machines in the node to communicate with them directly, rather than through the ServiceManagers.

## Specifications

A detailed description of Node Management objects follows.

### AGNodeService

The Node Service is the central repository of information about a Node.  The NodeService communicates with Service Managers on the machines in a Node to discover their resources and configure Services to deliver those resources to a Venue.  It communicates with Services to start, stop, and configure them.

| Attribute | Descriptions |
| --- | --- |
| name : string |  |
| description : string |  |
| uri : URIType |  |
| httpBaseUri : string |  |
| serviceManagers : AGServiceManagerDescription [ ] |  |
| services : AGServiceDescription [ ] |  |
| authorizedUsers : string [ ] |  |

| Method Signature | Description |
| --- | --- |
| AddAuthorizedUser( string user ) : None | user arg is DN |
| RemoveAuthorizedUser( string user ) : None | user arg is DN |
| AddServiceManager( AGServiceManagerDescription ) : None |  |
| RemoveServiceManager( AGServiceManagerDescription ) : None |  |
| GetServiceManagers() : AGServiceManagerDescription [ ] |  |
| GetResources() : MediaResource [ ] |  |
| GetAvailableServices() : AGServiceImplementation [ ] |  |
| GetServices() : AGServiceDescription [ ] |  |
| ConfigureStreams( StreamDescription [ ] ) : None |  |
| GetCapabilities() : Capability [ ] |  |

### AGServiceManager

An AGServiceManager resides on a machine “in” the Node, to provide information about the machine’s resources to the NodeService, and to respond to requests from the NodeService to configure AGServices to deliver those resources.

| Attribute | Descriptions |
| --- | --- |
| name : string |  |
| description : string |  |
| uri : URIType |  |
| mediaResources : MediaResource [ ] |  |
| services : AGServiceDescription [ ] |  |
| authorizedUsers : string [ ] |  |

| Method Signature | Description |
| --- | --- |
| GetResources() : MediaResource [ ] |  |
| - AddResource( MediaResource ) : None |  |
| DiscoverResources() : None |  |
| AddService( AGServiceImplementation, MediaResource ) : None |  |
| RemoveService( AGServiceDescription ) : None |  |
| GetServices() : AGServiceDescription [ ] |  |
| SetAuthorizedUsers( string [ ] users ) : None |  |

### AGServiceManagerDescription

| Attribute | Descriptions |
| --- | --- |
| name : string |  |
| description : string |  |
| uri : URIType |  |

### AGService

To allow the client to configure services generally, a service provides access to its configurable parameters as a list (see Service Configuration), and accepts a list to set the configuration.

| Attribute | Descriptions |
| --- | --- |
| name : string |  |
| description : string |  |
| uri : URIType |  |
| mediaResource : MediaResource |  |
| inputStreamConfiguration : StreamDescription |  |
| outputStreamConfiguration : StreamDescription |  |
| capabilities : Capability [ ] |  |
| authorizedUsers : string [ ] |  |
| isStarted : int |  |

| Method Signature | Description |
| --- | --- |
| Start() : None |  |
| Stop() : None |  |
| SetAuthorizedUsers( string [ ] users ) : None |  |
| GetCapabilities() : Capability [ ] |  |
| GetResource() : MediaResource |  |
| SetResource( MediaResource ) : None |  |
| GetConfiguration() : Parameter [ ] |  |
| SetConfiguration( Parameter [ ] ) : None |  |
| ConfigureStream( StreamDescription ) : None |  |
| IsStarted() : int |  |

### AGServiceDescription

| Attribute | Descriptions |
| --- | --- |
| name : string |  |
| description : string |  |
| uri : URIType |  |
| capabilities : Capability [ ] |  |

### AGServiceImplementation

| Attribute | Descriptions |
| --- | --- |
| name : string |  |
| description : string |  |
| uri : URIType | URL of Service Implementation |
| capabilities : Capability [ ] |  |
| platform : string |  |
| commandLineArgs : string |  |

### Parameter

| Attribute | Descriptions |
| --- | --- |
| name : string |  |
| value : string |  |
| type : const == PARAMETER |  |

### RangeParameter

| Attribute | Descriptions |
| --- | --- |
| name : string |  |
| value : float |  |
| type : const == RANGE_PARAMETER |  |
| lowerBound : float |  |
| upperBound : float |  |

### OptionSetParameter

| Attribute | Descriptions |
| --- | --- |
| name : string |  |
| value : string |  |
| type : const == OPTION_SET_PARAMETER |  |
| options : string [ ] |  |

### Capability

| Attribute | Descriptions |
| --- | --- |
| role : string | (PRODUCER, CONSUMER) |
| type : string | (AUDIO, VIDEO, TEXT, … ) |
| parms : dict() |  |

### MediaResource

| Attribute | Descriptions |
| --- | --- |
| type : string | (AUDIO, VIDEO, …) |
| resource : string | e.g., host:/dev/device |

## Glossary

## References

Notes

- This document sorely needs sequence diagrams to tie the data together into an understandable form.